TeleMetrum Low-level Access
- CC1111 4-wire debug interface:
  - debug data, debug clock, reset, ground
- CP2103 -- 4 GPIOs controlled from USB
  - One USB packet per half clock
- Beagle USB hardware monitor
- CC1111-based debug link
  - emulates serial on USB
  - provides high-level commands

---
TeleMetrum Software Development Environment
- Small Device C Compiler, targeting 8051 CPU
- Source Debugger for SDCC
- Hex debugger using either CP2103 or CC1111 link
  - Emulates mcs51 emulator
  - Except talks to real hardware
  - Hooks up to sdcdb

---
AltOS architecture
- Multi-threaded
  - Avoids the 'one big loop'
- Non pre-emptive
  - Limits where pre-emption can occur
- sleep/wakeup rendezvous
  - Good enough for Unix
- Timers, mutexes
- Basic OS services

---
AltOS Flight software architecture
- Flight progress tracked through discrete states
- Connect to host via USB serial emulation
  - No kernel driver required
  - Command line interface
  - Also works over radio link
- Configuration stored in EEPROM/Flash

---
AltOS Flight States
- Pad - Sitting vertically
- Boost - Acceleration > 2g and Speed > 5m/s or Height > +20m
- Fast - Acceleration < -1/4 or Boost period > 15s
- Coast - Speed < 200m/s or Height < Max_height - 500m
- Apogee - Height < Max Height - 10m
- Main - Height < Main Height
- Land - Acceleration stable for 5 seconds and Height stable for 5 seconds and Height < Launch height + 1000m

---
AltOS Hardware Calibration
- Radio calibrated by adjusting PLL against freq counter
  - 48MHz crystal good to 20ppm
  - 20ppm at 434MHz is 9Khz
- Accelerometer calibrated by rotating board on bench
  - Accelerometer output runs through 5V->3.3V divider
  - Uses 1% resistors
  - Also automatically adjusts for 100G/50G/40G devices

---
GPS adventures
- Problem: GPS looses satellites during boost phase
- GPS receivers track sats by synthesizing expected signal
  - Frequency based on relative velociy
  - Phase based on distance
- Change in actual signal means changing synthetic signal
- High acceleration means allowing faster changes
- Change rate limited by 'loop filter' bandwidth.