ChaosKey v1.0 Test Plan v1.0

keithp@keithp.com

Altus Metrum, LLC

2016/05/04

| Data | Version | Introduction | Author |
| --- | --- | --- | --- |
| 2016/05/04 | V1.0 | First version | keithp |

1. Product Introduction

ChaosKey is a hardware random number generator. The noise source is a reverse-biased transistor junction which generates broad spectrum white noise when driven above the breakdown voltage. ChaosKey incorporates a 20V power supply which drives the transistor to generate approximately 20mV of noise. This is amplified by a high-bandwidth op amp by 20dB and sampled at 1MHz by the SoC's ADC.

2. Test theory

- Assemble boards with STM32F042G6U6 processor

- Connect via USB to computer

- Verify that device registers as new USB device to operating system

- Disconnect device

3. Test tools

Hardware:

- ChaosKey with STM32F042G6U6 processor

Software:

- None

5. Test procedure

5.1 Test Preparation procedure

- The STM32F042G6U6 is provided with a built-in boot loader which communicates with the host over USB.

- Connect the ChaosKey device to a computer via USB.

5.2 Testing procedure

1.)  Verify that the ChaosKey appears as a new device to the computer operating system.

6. Test result

Please record the test results and defective phenomena.