Title
Building Better Electronic Bays
Bdale Garbee
TRA 12201 L3

---
Agenda
- Planning and building an electronic bay
- Considerations when radios are involved
- Finding your rocket using GPS

---
Subtitle - Planning
Planning

---
Things to Think About Before You Start Building
- What electronics are we talking about?
- Where in the airframe?
- External connections required?
- Component orientation
- Batteries, switches, connectors

---
Mechanical Considerations
- Keep charge gasses away from electronics!
- Couplers
  - Many rockets use an electronics bay in a coupler that needs to carry recovery system loads
  - Lifting eyes / eye nuts on all-thread instead of separate eye bolts or u-bolts un-loads bulkheads, frees up space
- Alignment / orientation of sensors
- Switch plungers orthogonal to axis of flight!
- Mounting batteries

---
Subtitle - Planning
Radios

---
Radios in Rockets
- GPS receiver
- Telemetry transmitter / telecommand receiver
- Video transmitters
- Stand-alone GPS tracker / RDF transmitters

---
What’s Different With Radios?
- Does airframe pass radio signals?
  - Challenges with carbon fiber, metal-bearing paints
- Impact of nearby metal, other components
- Mechanical issues with antennas
- Radiated emission impact on other electronics
  - Twist wire pairs to minimize signal pick-up!
  - Avoid putting high-power transmitters to close to devices controlling energetics!

---
Ground Testing
- To confirm RF emissions aren’t affecting pyro events, test with e-matches but no BP
- Use ground station “RSSI” to determine radiated signal pattern, compare different configurations, confirm flight readiness
- Radio-equipped Altus Metrum products support ground testing ejection charges over radio

---
Subtitle - Planning
Finding a Rocket with GPS

---
Rocket Recovery with GPS
- Confirm solid GPS lock before launch
- During flight, GPS data in telemetry can help you know where to look to visually track rocket .. Altus Metrum ground stations provide voice updates so you can watch rocket in flight
- After landing, use last reported GPS position as location to start search .. AltosDroid provides handy “walk me to my rocket” voice features

---
No Signal After Apogee Event?
- A “common” GPS failure mode is when something causes radio to stop transmitting during flight, often after apogee event
- Plotting GPS position data from the telemetry received can help guide recovery efforts
  - Where was the last data point?
  - How was airframe moving at that time?
  - What were winds like?
  - Estimating likely landing area

---
How High Did It Go?
- Most flight computers use baro sensors to measure and report apogee altitude, using a “standard model” of the atmosphere.
- Baro sensors max out around 30km up
- If the apogee is high enough for GPS lock to be solidly re-established after motor burnout, and retained through apogee, the GPS apogee determination is more accurate
- Tripoli requires GPS for records above 30k’ MSL

---
https://altusmetrum.org

---
GPS
- Radio receiver listening to GPS satellites
  - Satellites send precise timing and satellite orbit info
  - Receiver works out where it must be for arrival times of the different signals to make sense
  - X, Y, Z, and time .. at least 4 satellites needed
- “Anti-SCUD” rules limit velocity & altitude
- Consumer receivers not meant for high dynamics
  - Virtually impossible to retain lock under high acceleration
- Best solution we have for knowing where the rocket is during and after flight
- u-blox 7 series currently best in class for rockets

---
Sensor Combinations
- Individual sensors always have limits, combining sensors in software can give better results
  - Baro better than GPS during boost, GPS better up high
- Kalman filtering is an approach to “sensor fusion” that provides outstanding results, and is used in all Altus Metrum flight computers
- Combinations of acceleration, rotation, and magnetic sensors are often refered to as an “IMU” or inertial measurement unit
  - Accelerometers can tell you pre-launch orientation
  - Gyros can tell you rotation about each axis in flight