Hardware
Electronics in
Hobby Rockets
Bdale Garbee
NAR 87103 / TRA 12201 L3

---
Agenda
- Electronics in rockets
- Sensors
- Dual deployment

---
Electronics in Rockets
- Airframe recovery
  - Deploying parachutes
  - Finding the airframe
- Collecting flight performance data
  - Calibrating simulations
  - Characterize research motors
- Payloads
  - Cameras, science experiments, etc
- Control complex flights
  - Multi-stage, air starts, clusters, etc

---
Airframe Recovery
- Parachute deployment
  - Deploy at apogee
  - Deploy at a programmed height above ground
- Finding the airframe
  - Noise makers
  - Beacons for radio direction finding (RDF, “fox hunting”)
  - GPS

---
Performance Data
- Even simple data can be fun to know
  - How high did it go?
  - How fast did it go?
- Calibrating simulations
  - Calibrate drag coefficient using actual flight data
- Characterize research motors
  - Compare acceleration to simulation results
  - Measure chamber pressure and temperatures

---
Electronic Payloads
- Video and still-frame cameras
- Science experiments
  - Temperature rise in nose and fins above Mach
  - Exploring behavior of new sensors
- Satellites and landers
  - CANSAT
  - ARLISS

---
Complex Flights
- Multi-stage
  - Triggering separation
  - Igniting upper stage motor(s)
- Air Starts
  - Igniting additional motors in flight
- Clusters
  - Can treat high power clusters like air starts
- Complex flights pose additional safety risks
  - Only ignite additional motors if flight is nominal

---
Hardware
Sensors

---
Sensor Types
- Time
- Temperature
- Air pressure
- Acceleration
- Rotation
- Magnetic
- Light
- GPS

---
Sensing Time
- Electronic timers
  - Usually based on quartz crystal reference
  - Essentially just a fancy pulse counter
- Need some mechanism for detecting launch
  - Old-school approach was often a “break wire”
  - G-switches
  - Integration with other flight avionics
- Events programmed to happen at specific times
  - Far more reliable than motor delay grains...
  - What happens if flight isn't nominal?

---
Temperature
- Thermistors
  - Basically a resistor that changes value with temperature
  - Positive or negative temperature coefficients
  - Good for most hobby rocketry uses
- Thermocouples
  - Two dis-similar metals in contact with each other
  - Produce tiny voltage with temperature difference
  - Can measure very high temperatures, thus can be useful for motor characterization
- Digital temperature measuring integrated circuits
- All analog temperature sensors must be calibrated

---
Air Pressure
- MEMS barometric sensors
- Have finite range and accuracy
  - Lowest useful pressure measurable limits max altitude
  - Resolution and noise of sensor limit accuracy
- Converting pressure to altitude
  - Standard model of the atmosphere, temp dependent
- Only really useful for relative altitudes
  - Calibrate “starting elevation” while waiting for launch
- Can be “fooled” by Mach transitions, etc
- MS5607 works to 30km, 20cm at sea level!

---
Acceleration
- MEMS acceleration sensors
- Have finite range and accuracy
  - Plus and minus maximum G ratings
  - Resolution and noise of sensor limit accuracy
- Sampling rate
- 3-axis sensors with ranges up to about 18g
- Single-axis sensors to 200g or more

---
Rotation
- MEMS gyros
- Have finite range and accuracy
  - Plus and minus limits in degrees / second
  - Resolution and noise of sensor limit accuracy
- Sampling rate
- 3-axis sensors with ranges up to 2000 deg/sec

---
Magnetism
- MEMS compass
- Measures influence of Earth's magnetic field
- Readings are noisy
- Must be calibrated before flight
- Nearby metal alters readings due to eddy currents
  - Launch rods and rails

---
Light
- Photo cells
- Photovoltaic (solar) cells
- Mostly a curiosity...
- Possible to detect rotation rates
- Possible to detect passing through cloud layers

---
GPS
- Radio receiver listening to GPS satellites
  - Satellites send precise timing and satellite orbit info
  - Receiver works out where it must be for arrival times of the different signals to make sense
  - X, Y, Z, and time .. at least 4 satellites needed
- “Anti-SCUD” rules limit velocity & altitude
- Consumer receivers not meant for high dynamics
  - Virtually impossible to retain lock under high acceleration
- Best solution we have for knowing where the rocket is during and after flight
- u-blox 7 series currently best in class for rockets

---
Sensor Combinations
- Individual sensors always have limits, combining sensors in software can give better results
  - Baro better than GPS during boost, GPS better up high
- Kalman filtering is an approach to “sensor fusion” that provides outstanding results, and is used in all Altus Metrum flight computers
- Combinations of acceleration, rotation, and magnetic sensors are often refered to as an “IMU” or inertial measurement unit
  - Accelerometers can tell you pre-launch orientation
  - Gyros can tell you rotation about each axis in flight

---
Hardware
Dual Deploy

---
What is Dual Deploy?
- A very useful approach to recovering airframes closer to the launch site
  - First event at apogee where kinetic energy is minimal
  - Second event at a programmed altitude above ground
- Drogue or drogueless descent from apogee
  - Rapid descent for minimal drift down-wind
  - Controlled, not ballistic, descent!
- Final descent under larger “main” parachute
  - Minimize damage to airframe
  - Safety

---
What's Needed?
- Airframe designed for two deployments
  - Most often done by having two bays and break points
  - Can do dual deploy from one bay
- Electronics bay
  - Sealed from exhaust gases
  - Static pressure port to outside air
  - Accessible power switch
- Flight Computer with at least 2 pyro channels
- Low-current electric matches or Q2G2 igniters
- Black powder
- Charge holding materials

---
Important Details
- Black powder charge sizing
  - Depends on bay dimensions and desired force
  - Too little and deployment fails to occur
  - Too big and airframe will be damaged
- Static port sizing
  - Critical for baro-only flight computers
  - Too small and pressure change “lags” at sensor
  - Too large and turbulence may result
  - Important for holes to be “clean” to avoid turbulence

---
Important Details
- Use shear pins to prevent drag separation
  - Suitable airframe material (cardboard tubes may tear)
  - 2-56 nylon screws and small polystyrene rod work well
  - Include force to shear pins in black powder calculation
- Redundant electronics (required for L3 certs)
  - Use “apogee delay” on one altimeter to prevent simultaneous firing
  - Set main deployment altitudes to different heights

---
Resources
- Altus Metrum, http://altusmetrum.org
  - Bdale and Keith's company .. open source avionics
- Rocketry Online, http://www.info-central.org
  - BP calculations, static port sizing, etc
- Electronic payload competitions
  - CANSAT, http://cansatcompetition.com
  - ARLISS, http://www.arliss.org